## Slide 1: Tier 5 Workgroup: In-Use Program Concepts May 2, 2022

## Slide 2: Zoom Webinar Details
Telephone Call-in: (216) 706 – 7005
Access Code: 400363
Questions
  In Zoom: Use the “Raise Hand” feature, or type in “Q&A” box
  On phone:
    #2 to “Raise Hand”
    *6 to unmute/mute

## Slide 3: Agenda
 | Topic | Presenter
1. | Opening Remarks | Kim Heroy-Rogalski & Jenna Latt
2. | Presentation: Tier 5 In-Use Concepts | Christian Bartolome
3. | Questions and Discussion | 
4. | Next Steps, Announcements and Closing | 

## Slide 4: Outline
Current California Air Resources Board (CARB) Off-Road
In-Use Compliance (ORIUC) Program
Proposed Changes to CARB ORIUC Program
Background re: Heavy-Duty In-Use Testing (HDIUT)
Manufacturer run Off-Road In-Use Testing (ORIUT) Program Concept
  Proposed Reporting
  Proposed Pass/Fail Criteria
Portable Emissions Measurement System (PEMS) Testing Challenges and Solutions
Feedback Requested

## Slide 5: Current CARB ORIUC Program
CARB staff currently has the authority to conduct in-use testing on off-road engines 13 CCR 2139(g)
Off-road engines are evaluated with test procedures used at certification:
  Transient, steady state, and not-to-exceed
Off-road engines may be tested up to 75% of Useful Life (UL)

## Slide 6: Proposed Changes to CARB’s ORIUC Program
  Clean up language for ORIUC
  Off-Cycle Test Procedures with PEMS
  Updating emissions calculation and evaluation methods
  Considering changes to expand the UL limits for ORIUC test engines

## Slide 7: Manufacturer-run ORIUT
In-Use Testing background
ORIUT Concept
  Phase 1: Engine Control Unit (ECU)/sensors data submission and screening
  Phase 2: Triggered PEMS testing
  Phase 3: Corrective action and long-term PEMS testing, if needed

## Slide 8: Background: In-Use Testing
Manufacturer run in-use testing programs
  On-Road Heavy Duty Diesel Engines
    Heavy-duty diesel engines non-compliance was discovered
    Settlement/consent decrees
    40 CFR 86 Subpart T
  Large Nonroad Spark Ignition Engines
    40 CFR Part 1048
    Additionally has production line testing and selective enforcement audits
Currently, manufacturer run in-use program does not exist for:
  On-road Otto engines
  Off-road compression ignition engines
    Selective Enforcement Audits (13 CCR 2427 & 40 CFR 1068 Subpart E)

## Slide 9: ORIUT Program Concept
Minimize cost while ensuring accurate emissions data
A multiphase approach would allow us to screen large volumes of sold engines with ECU/sensors data at a lower cost compared to PEMS testing
More accurate PEMS methods would be used for real world emissions assessment if triggered by screening results
Manufacturer run ORIUT with PEMS would be conducted for engine families not passing screening
Targeting ≥56 kW engines which at minimum would require Selective Catalytic Reduction (SCR) to comply

## Slide 10: Concept for Manufacturer-Run ORIUT Program
Manufacturers submit annual summary report of sensors/ECU/ Off-Road Real Emissions Assessment Logging (OR-REAL) data per engine
Borrows elements implemented in the In-Use Vehicle Emissions reporting from the extended durability program for on-road
Data collection would be conducted with telematics

## Slide 11: Flow Chart of ORIUT Concept
Step 1: ECU / Sensors data screening
  Manufacturers would annually submit data for 75% of engine sales per engine family (EF)
  Emissions data would be binned into idle, low load, or high load bins
  CARB staff would review reports for high emitters by bin
  If data for an EF raises no alerts, then the in-use testing requirements for the EF would be fulfilled
Step 2: Off-cycle testing with PEMS
  An EF flagged from screening would be required to conduct in-use testing like the on-road manufacturer requirements (5 to 10 engine tests with PEMS)
  If compliance is determined, then the in-use testing requirements would be fulfilled
Step 3: Corrective Action (if needed)
  If PEMS testing shows an EF is not compliant, then the manufacturer must take steps to correct the non-compliance

## Slide 12: Concept for Manufacturer-Run ORIUT Program
Manufacturers would submit data for a minimum of 75% of CA certified engines sold for each EF in California.
Manufacturer must submit all collected data
Data reports are not required for engines exceeding their useful life
Staff would use this information to screen for engine families with binned emissions greater than twice the emission standards for Low Load and Nonroad Transient Cycle (NRTC).
  Currently evaluating how to handle idle.

## Slide 13: What Reporting Would be Included ?
EF name
CA sales volume for EF
Rated engine power (kilowatt)
Engine Serial number
Engine run time (hours)
Date of data collection
Tracking parameters in OR-REAL details to be determined
  Tables 1 and 2 show hypothetical examples of OR-REAL tracking arrays and bin structure
 | Vehicle Speed (km/h) |  |  |  |  |  |  | 
% of Rated Power | > 0 ≤64 | 0 | > 0 ≤16 | > 16 ≤40 | > 40 ≤64 | > 64 |  | 
≤ 25% | bin 1 | bin 2 | bin 3 | bin 4 | bin 5 | bin 6 |  | 
>25 % ≤50% |  |  | bin 7 | bin 8 | bin 9 | bin10 |  | NTE Bin Bin 15
>50 % |  |  | bin 11 | bin 12 | bin 13 | bin 14 |  | Regen Bin Bin 16
Parameter | Active 100 Hour Array | Stored 100 Hour Array | Lifetime Array | Lifetime Engine Activity Array5
NOx mass - engine out1(g) | x | x | x | n/a
NOx mass – tailpipe2 (g) | x | x | x | n/a
Engine output engergy3 (kWh) | x | x | x | x
Distance Traveled (km) | x | x | x | x
Engine runtime (hour) | x | x | x | x
Vehicle fuel consumption4 (liters) | x | x | x | x
Table 1. NOx Tracking Arrays and Parameters
Table 2. Bin Structure for Each parameter in Each Array
1. Mass of NOx emitted by the engine upstream of the NOx emission control system.
2. Mass of NOx emitted by the engine which enters the atmosphere (downstream of the NOx emission control system )
3. Brake work output of the engine.
4. The amount of fuel consumed by the engine summed with the amount of fuel injected directly into the aftertreatment system.
5. Engine activity data are recorded regardless of NOx senor status.

## Slide 14: When Would Manufacturer Off-Road PEMS Testing Be Required?
For each EF selected, for each report, CARB would evaluate emissions vs the nitrogen oxides (NOx) emission standards for each of the bins (Low Load and NRTC)
If 20% or more of the reports for an EF have events in any bin with emissions greater than 2 times the emission standard, then the engine manufacturer would be required to conduct ORIUT with PEMS (Step 2)
Notes: if we have manufacturer/3rd party do the testing the trigger for off-road in-use PEMS testing should be clear. here in this draft i suggest 20% failure would cause concern similar to pass fail criteria of 8/10 engines fail. another possible percentage to place in there could be 5% since EWIR uses that as a trigger from warranty claims

## Slide 15: Proposed Pass and Fail criteria
Similar structure to the on-road program (40 CFR 86 subpart T)
Emissions evaluation method: in development
  Looking into using binned moving average window emissions evaluation methodology
Start with 5 engines and if 5 pass, then EF passes
  5/6 pass tests  EF pass
  If 2/6 fail  4 more engines tested (total 10)
  Less than 8 engines passing would be considered EF failure
If an EF fails, then corrective action would be required
Additionally, failing EFs would require ORIUT with PEMS every 2 to 4 years

## Slide 16: PEMS Testing Challenges and Solutions
Standardized connection and data stream protocols
Location for mounting on off-road equipment and safety considerations
  Creative mounting solutions for mounting (ex. roof)
  Special harnesses or bolt down options
  CARB staff and European Union have conducted testing on some equipment with PEMS mounted to following golf cart
Some PEMS is approximately the size of the equipment
  Consideration of compact PEMS for such applications
Vibration and impact resistance
  Require more data on forces from real world scenarios

## Slide 17: Feedback Requested
  Alternative manufacturer-run concepts
  Power category and equipment type applicability
  Is a sensors-based program attractive to industry?
  Defining bins for sensors reporting
  Standardization of ECU communication
  OBD OR-REAL program for off-road applications
  In-use emissions data evaluation methods
  Off-road off-cycle emissions testing with PEMS
  Other comments

## Slide 18: Zoom Webinar Details
Telephone Call-in: (216) 706 – 7005
Access Code: 400363
Questions
  In Zoom: Use the “Raise Hand” feature, or type in “Q&A” box
  On phone:
    #2 to “Raise Hand”
    *6 to unmute/mute