## Source Profiles

The source types that contribute to PM10 in the San Joaquin Valley Air Basin are:

- Geological material (fugitive dust from paved and unpaved roads, agriculture, construction, and vacant land).

- Motor vehicle (exhaust, tire and break wear).

- Vegetative burning (residential wood burning and agricultural burning).

- Secondary particles (ammonium sulfate, ammonium nitrate, and organic compounds).

For each source type listed above, several subtypes were evaluated using CMB, including break and tire wear, cooking, natural gas combustion, oil combustion, tire burning, and several subcategories of geological material (paved and unpaved road dust, agricultural operations, and construction).  Since some of the source subtypes could not be distinguished from other sources, composite profiles were created to best represent the mixture of sources.  Each of the composite profiles includes sources that are not easily distinguishable using commonly measured chemical species.  Table 1 and Table 2 show the chemical composition of source profiles that were selected for CMB modeling.

Table 1. Fugitive Dust Source Profiles for CMB Modeling

| Area/Month |  | Generic for SJV |  | Bakersfield/November |  | Bakersfield/January |  | Corcoran/December |  | Corcoran/December |  | Corcoran/January |  | Fresno/October |  | Fresno/December |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mnemonics |  | DUST |  | FDBACNOV |  | FDBACJAN |  | FDCOPOCT |  | FDCOPDEC |  | FDCOPJAN |  | FDFREOCT |  | FDFREDEC |
| Chloride (Cl-) |  | 0.1327 | ± | 0.2849 |  |  | ± |  |  |  | ± |  |  | 0.2835 | ± | 0.5787 |  | 0.2420 | ± | 0.5787 |  | 0.2548 | ± | 0.5787 |  |  | ± |  |  |  | ± |  |
| Nitrate (NO3-) |  | 0.0973 | ± | 0.4209 |  | 0.0350 | ± | 0.1515 |  | 0.0450 | ± | 0.2253 |  | 0.1205 | ± | 0.6197 |  | 0.1205 | ± | 0.6197 |  | 0.1205 | ± | 0.6197 |  | 0.0263 | ± | 0.3193 |  | 0.0000 | ± | 0.3361 |
| Phosphate (PO42-) |  | 0.2754 | ± | 0.8106 |  |  | ± |  |  |  | ± |  |  | 0.5333 | ± | 1.7778 |  | 0.3556 | ± | 1.7778 |  | 0.3556 | ± | 1.7778 |  |  | ± |  |  |  | ± |  |
| Sulfate (SO42-) |  | 0.6224 | ± | 1.0766 |  | 0.3754 | ± | 0.2596 |  | 0.3232 | ± | 0.3198 |  | 0.3508 | ± | 0.2806 |  | 0.3395 | ± | 0.2806 |  | 0.3520 | ± | 0.2806 |  | 0.5145 | ± | 0.8244 |  | 0.5223 | ± | 0.8305 |
| Ammonia (NH3) |  |  | ± |  |  |  | ± |  |  |  | ± |  |  |  | ± |  |  |  | ± |  |  |  | ± |  |  |  | ± |  |  |  | ± |  |
| Ammonium (NH4+) |  | 0.1299 | ± | 0.1618 |  | 0.2152 | ± | 0.1737 |  | 0.2990 | ± | 0.3021 |  | 0.1800 | ± | 0.1348 |  | 0.2148 | ± | 0.1348 |  | 0.2363 | ± | 0.1348 |  | 0.0388 | ± | 0.1964 |  | 0.0285 | ± | 0.1009 |
| Soluble Sodium (NA+) |  | 0.2484 | ± | 0.4924 |  | 0.1789 | ± | 0.2218 |  | 0.0878 | ± | 0.0342 |  | 0.1805 | ± | 0.2466 |  | 0.1593 | ± | 0.2466 |  | 0.1631 | ± | 0.2466 |  | 0.1434 | ± | 0.0792 |  | 0.1838 | ± | 0.0717 |
| Soluble Potassium (K+) |  | 0.3263 | ± | 0.7110 |  | 0.5295 | ± | 1.1328 |  | 0.1576 | ± | 0.0487 |  | 0.4726 | ± | 1.2942 |  | 0.3428 | ± | 1.2942 |  | 0.3431 | ± | 1.2942 |  | 0.2586 | ± | 0.1327 |  | 0.2896 | ± | 0.1784 |
| Organic Carbon (OC) |  | 5.3827 | ± | 5.6885 |  | 9.3529 | ± | 5.6752 |  | 8.9405 | ± | 1.9850 |  | 5.3912 | ± | 7.3384 |  | 4.8679 | ± | 7.3384 |  | 5.0408 | ± | 7.3384 |  | 13.3915 | ± | 9.7731 |  | 15.8953 | ± | 12.6384 |
| Elemental Carbon (EC) |  | 0.3004 | ± | 0.4994 |  | 0.9039 | ± | 0.6569 |  | 1.2035 | ± | 1.0945 |  | 0.2101 | ± | 0.5069 |  | 0.2530 | ± | 0.5069 |  | 0.2894 | ± | 0.5069 |  | 1.7795 | ± | 1.5030 |  | 2.1829 | ± | 1.7928 |
| Total Carbon (TC) |  | 5.6830 | ± | 5.8802 |  | 10.2568 | ± | 5.7423 |  | 10.1440 | ± | 2.4890 |  | 5.6013 | ± | 7.3937 |  | 5.1208 | ± | 7.3937 |  | 5.3302 | ± | 7.3937 |  | 15.1709 | ± | 11.2605 |  | 18.0782 | ± | 14.4313 |
| Sodium (Na) |  | 0.3196 | ± | 0.4767 |  |  | ± |  |  |  | ± |  |  | 0.2199 | ± | 0.1604 |  | 0.2309 | ± | 0.1604 |  | 0.2410 | ± | 0.1604 |  |  | ± |  |  |  | ± |  |
| Magnesium (Mg) |  | 0.8458 | ± | 0.3210 |  |  | ± |  |  |  | ± |  |  | 0.8965 | ± | 0.5879 |  | 0.8601 | ± | 0.5879 |  | 0.8795 | ± | 0.5879 |  |  | ± |  |  |  | ± |  |
| Aluminum (Al) |  | 10.1908 | ± | 3.0775 |  | 8.1747 | ± | 2.4168 |  | 8.8333 | ± | 2.1655 |  | 10.8805 | ± | 3.7354 |  | 11.5542 | ± | 3.7354 |  | 11.7950 | ± | 3.7354 |  | 10.1763 | ± | 2.7407 |  | 9.9183 | ± | 2.6088 |
| Silicon (Si) |  | 31.3412 | ± | 10.0444 |  | 23.5229 | ± | 6.6262 |  | 23.9450 | ± | 6.3233 |  | 30.1021 | ± | 9.9697 |  | 31.7208 | ± | 9.9697 |  | 32.3157 | ± | 9.9697 |  | 28.1285 | ± | 9.3525 |  | 25.2404 | ± | 7.5867 |
| Phosphorus (P) |  | 0.3342 | ± | 0.9102 |  |  | ± |  |  |  | ± |  |  | 0.6829 | ± | 1.9583 |  | 0.4914 | ± | 1.9583 |  | 0.4953 | ± | 1.9583 |  |  | ± |  |  |  | ± |  |
| Sulfur (S) |  | 0.4231 | ± | 0.8053 |  | 0.3989 | ± | 0.1901 |  | 0.4191 | ± | 0.1910 |  | 0.2550 | ± | 0.1902 |  | 0.2562 | ± | 0.1902 |  | 0.2723 | ± | 0.1902 |  | 0.4476 | ± | 0.3611 |  | 0.4467 | ± | 0.2593 |
| Chlorine (Cl) |  | 0.0953 | ± | 0.2767 |  | 0.3344 | ± | 0.4656 |  | 0.2008 | ± | 0.0580 |  | 0.1979 | ± | 0.5772 |  | 0.1387 | ± | 0.5772 |  | 0.1387 | ± | 0.5772 |  | 0.1043 | ± | 0.0915 |  | 0.1280 | ± | 0.1131 |
| Potassium (K) |  | 2.8914 | ± | 0.8919 |  | 3.0953 | ± | 1.4272 |  | 2.8273 | ± | 0.6454 |  | 3.1403 | ± | 1.4530 |  | 3.0957 | ± | 1.4530 |  | 3.1755 | ± | 1.4530 |  | 2.5731 | ± | 1.0187 |  | 2.0048 | ± | 0.3620 |
| Calcium (Ca) |  | 3.4219 | ± | 1.7163 |  | 4.3174 | ± | 2.9795 |  | 3.5278 | ± | 0.6505 |  | 3.1485 | ± | 1.8363 |  | 3.0366 | ± | 1.8363 |  | 3.0789 | ± | 1.8363 |  | 3.0455 | ± | 0.5108 |  | 2.9558 | ± | 0.7668 |
| Titanium (Ti) |  | 0.4157 | ± | 0.0731 |  | 0.4326 | ± | 0.2126 |  | 0.4890 | ± | 0.3041 |  | 0.4913 | ± | 0.1731 |  | 0.5282 | ± | 0.1731 |  | 0.5441 | ± | 0.1731 |  | 0.4922 | ± | 0.0624 |  | 0.4883 | ± | 0.0514 |
| Vanadium (V) |  | 0.0079 | ± | 0.0381 |  | 0.0141 | ± | 0.0236 |  | 0.0163 | ± | 0.0340 |  | 0.0080 | ± | 0.0303 |  | 0.0086 | ± | 0.0303 |  | 0.0089 | ± | 0.0303 |  | 0.0226 | ± | 0.0231 |  | 0.0264 | ± | 0.0144 |
| Chromium (Cr) |  | 0.0026 | ± | 0.0114 |  | 0.0090 | ± | 0.0131 |  | 0.0096 | ± | 0.0206 |  | 0.0011 | ± | 0.0096 |  | 0.0013 | ± | 0.0096 |  | 0.0014 | ± | 0.0096 |  | 0.0201 | ± | 0.0165 |  | 0.0254 | ± | 0.0163 |
| Manganese (Mn) |  | 0.0857 | ± | 0.0209 |  | 0.1046 | ± | 0.0721 |  | 0.1216 | ± | 0.1095 |  | 0.0772 | ± | 0.0135 |  | 0.0790 | ± | 0.0135 |  | 0.0806 | ± | 0.0135 |  | 0.1119 | ± | 0.0125 |  | 0.1036 | ± | 0.0225 |
| Iron (Fe) |  | 4.9351 | ± | 0.8115 |  | 5.1572 | ± | 2.4574 |  | 5.8896 | ± | 3.3036 |  | 5.5029 | ± | 1.7259 |  | 5.7237 | ± | 1.7259 |  | 5.7549 | ± | 1.7259 |  | 5.3027 | ± | 0.6624 |  | 5.4184 | ± | 0.6438 |
| Cobalt (Co) |  | 0.0010 | ± | 0.0779 |  |  | ± |  |  |  | ± |  |  | 0.0019 | ± | 0.0829 |  | 0.0027 | ± | 0.0829 |  | 0.0032 | ± | 0.0829 |  |  | ± |  |  |  | ± |  |
| Nickel (Ni) |  | 0.0032 | ± | 0.0043 |  | 0.0047 | ± | 0.0043 |  | 0.0048 | ± | 0.0052 |  | 0.0008 | ± | 0.0026 |  | 0.0008 | ± | 0.0026 |  | 0.0008 | ± | 0.0026 |  | 0.0066 | ± | 0.0055 |  | 0.0092 | ± | 0.0029 |
| Copper (Cu) |  | 0.0145 | ± | 0.0088 |  | 0.0175 | ± | 0.0064 |  | 0.0206 | ± | 0.0107 |  | 0.0111 | ± | 0.0055 |  | 0.0112 | ± | 0.0055 |  | 0.0115 | ± | 0.0055 |  | 0.0170 | ± | 0.0049 |  | 0.0191 | ± | 0.0033 |
| Zinc (Zn) |  | 0.0519 | ± | 0.0643 |  | 0.0808 | ± | 0.0492 |  | 0.1113 | ± | 0.0145 |  | 0.0622 | ± | 0.0500 |  | 0.0780 | ± | 0.0500 |  | 0.0891 | ± | 0.0500 |  | 0.1350 | ± | 0.0951 |  | 0.1402 | ± | 0.1055 |
| Gallium (Ga) |  | 0.0004 | ± | 0.0027 |  |  | ± |  |  |  | ± |  |  | 0.0012 | ± | 0.0019 |  | 0.0012 | ± | 0.0019 |  | 0.0012 | ± | 0.0019 |  |  | ± |  |  |  | ± |  |
| Arsenic (As) |  | 0.0016 | ± | 0.0030 |  |  | ± |  |  |  | ± |  |  | 0.0022 | ± | 0.0024 |  | 0.0020 | ± | 0.0024 |  | 0.0019 | ± | 0.0024 |  |  | ± |  |  |  | ± |  |
| Selenium (Se) |  | 0.0002 | ± | 0.0015 |  |  | ± |  |  |  | ± |  |  | 0.0002 | ± | 0.0010 |  | 0.0002 | ± | 0.0010 |  | 0.0002 | ± | 0.0010 |  |  | ± |  |  |  | ± |  |
| Bromine (Br) |  | 0.0013 | ± | 0.0013 |  | 0.0039 | ± | 0.0040 |  | 0.0048 | ± | 0.0053 |  | 0.0015 | ± | 0.0018 |  | 0.0013 | ± | 0.0018 |  | 0.0013 | ± | 0.0018 |  | 0.0068 | ± | 0.0053 |  | 0.0082 | ± | 0.0063 |
| Rubidium (Rb) |  | 0.0134 | ± | 0.0031 |  |  | ± |  |  |  | ± |  |  | 0.0145 | ± | 0.0026 |  | 0.0150 | ± | 0.0026 |  | 0.0153 | ± | 0.0026 |  |  | ± |  |  |  | ± |  |
| Strontium (Sr) |  | 0.0328 | ± | 0.0097 |  |  | ± |  |  |  | ± |  |  | 0.0302 | ± | 0.0079 |  | 0.0304 | ± | 0.0079 |  | 0.0306 | ± | 0.0079 |  |  | ± |  |  |  | ± |  |
| Yttrium (Y) |  | 0.0024 | ± | 0.0015 |  |  | ± |  |  |  | ± |  |  | 0.0030 | ± | 0.0011 |  | 0.0032 | ± | 0.0011 |  | 0.0033 | ± | 0.0011 |  |  | ± |  |  |  | ± |  |
| Zirconium (Zr) |  | 0.0104 | ± | 0.0032 |  |  | ± |  |  |  | ± |  |  | 0.0095 | ± | 0.0038 |  | 0.0105 | ± | 0.0038 |  | 0.0111 | ± | 0.0038 |  |  | ± |  |  |  | ± |  |
| Molybdenum (Mo) |  | 0.0012 | ± | 0.0037 |  |  | ± |  |  |  | ± |  |  | 0.0012 | ± | 0.0026 |  | 0.0009 | ± | 0.0026 |  | 0.0006 | ± | 0.0026 |  |  | ± |  |  |  | ± |  |
| Palladium (Pd) |  | 0.0004 | ± | 0.0228 |  |  | ± |  |  |  | ± |  |  | 0.0002 | ± | 0.0163 |  | 0.0002 | ± | 0.0163 |  | 0.0002 | ± | 0.0163 |  |  | ± |  |  |  | ± |  |
| Silver (Ag) |  | 0.0007 | ± | 0.0268 |  |  | ± |  |  |  | ± |  |  | 0.0000 | ± | 0.0192 |  | 0.0000 | ± | 0.0192 |  | 0.0000 | ± | 0.0192 |  |  | ± |  |  |  | ± |  |
| Cadmium (Cd) |  | 0.0014 | ± | 0.0283 |  |  | ± |  |  |  | ± |  |  | 0.0003 | ± | 0.0203 |  | 0.0003 | ± | 0.0203 |  | 0.0003 | ± | 0.0203 |  |  | ± |  |  |  | ± |  |
| Indium (In) |  | 0.0003 | ± | 0.0318 |  |  | ± |  |  |  | ± |  |  | 0.0001 | ± | 0.0228 |  | 0.0000 | ± | 0.0228 |  | 0.0000 | ± | 0.0228 |  |  | ± |  |  |  | ± |  |
| Tin (Sn) |  | 0.0062 | ± | 0.0399 |  |  | ± |  |  |  | ± |  |  | 0.0017 | ± | 0.0286 |  | 0.0016 | ± | 0.0286 |  | 0.0016 | ± | 0.0286 |  |  | ± |  |  |  | ± |  |
| Antimony (Sb) |  | 0.0079 | ± | 0.0467 |  |  | ± |  |  |  | ± |  |  | 0.0024 | ± | 0.0333 |  | 0.0027 | ± | 0.0333 |  | 0.0030 | ± | 0.0333 |  |  | ± |  |  |  | ± |  |
| Barium (Ba) |  | 0.0758 | ± | 0.1517 |  |  | ± |  |  |  | ± |  |  | 0.0679 | ± | 0.1088 |  | 0.0719 | ± | 0.1088 |  | 0.0739 | ± | 0.1088 |  |  | ± |  |  |  | ± |  |
| Lanthanum (La) |  | 0.0432 | ± | 0.2225 |  |  | ± |  |  |  | ± |  |  | 0.0257 | ± | 0.1585 |  | 0.0249 | ± | 0.1585 |  | 0.0247 | ± | 0.1585 |  |  | ± |  |  |  | ± |  |
| Gold (Au) |  | 0.0003 | ± | 0.0055 |  |  | ± |  |  |  | ± |  |  | 0.0001 | ± | 0.0042 |  | 0.0001 | ± | 0.0042 |  | 0.0001 | ± | 0.0042 |  |  | ± |  |  |  | ± |  |
| Mercury (Hg) |  | 0.0007 | ± | 0.0033 |  |  | ± |  |  |  | ± |  |  | 0.0007 | ± | 0.0023 |  | 0.0007 | ± | 0.0023 |  | 0.0007 | ± | 0.0023 |  |  | ± |  |  |  | ± |  |
| Thallium (Tl) |  | 0.0004 | ± | 0.0032 |  |  | ± |  |  |  | ± |  |  | 0.0005 | ± | 0.0022 |  | 0.0005 | ± | 0.0022 |  | 0.0005 | ± | 0.0022 |  |  | ± |  |  |  | ± |  |
| Lead (Pb) |  | 0.0056 | ± | 0.0060 |  | 0.0572 | ± | 0.2865 |  | 0.0593 | ± | 0.1018 |  | 0.0067 | ± | 0.0063 |  | 0.0075 | ± | 0.0063 |  | 0.0080 | ± | 0.0063 |  | 0.1718 | ± | 0.1458 |  | 0.2089 | ± | 0.1807 |
| Uranium (U) |  | 0.0014 | ± | 0.0035 |  |  | ± |  |  |  | ± |  |  | 0.0015 | ± | 0.0026 |  | 0.0018 | ± | 0.0026 |  | 0.0021 | ± | 0.0026 |  |  | ± |  |  |  | ± |  |

Fugitive Dust Source Profiles for CMB Modeling (Continued)

| Area/Month |  | Modesto/January |  | Oildale/January |  | Turlock/October |  | Fresno/Annual |  | Hanford/Annual |  | Kern Co./Annual |  | Visalia/Annual |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mnemonics |  | FDM14 |  | FDOIL |  | FDTUR |  | FDFREANN |  | FDHANANN |  | FDKERANN |  | FDVCSANN |
| Chloride (Cl-) |  | 0.1063 | ± | 0.1804 |  |  | ± |  |  | 0.1291 | ± | 0.2370 |  |  | ± |  |  | 0.2905 | ± | 0.5786 |  |  | ± |  |  |  | ± |  |
| Nitrate (NO3-) |  | 0.0000 | ± | 0.1778 |  | 0.1728 | ± | 0.5612 |  | 0.0398 | ± | 0.2332 |  | 0.0177 | ± | 0.2788 |  | 0.0602 | ± | 0.6220 |  | 0.0500 | ± | 0.1635 |  | 0.5350 | ± | 0.8801 |
| Phosphate (PO42-) |  | 0.0000 | ± | 0.0000 |  |  | ± |  |  | 0.0223 | ± | 0.0536 |  |  | ± |  |  | 0.5333 | ± | 1.7778 |  |  | ± |  |  |  | ± |  |
| Sulfate (SO42-) |  | 0.3946 | ± | 0.2246 |  | 0.4374 | ± | 0.3109 |  | 0.5824 | ± | 0.5262 |  | 0.5603 | ± | 0.7158 |  | 0.2801 | ± | 0.3278 |  | 0.4664 | ± | 0.2869 |  | 0.2725 | ± | 0.3582 |
| Ammonia (NH3) |  |  | ± |  |  |  | ± |  |  |  | ± |  |  |  | ± |  |  |  | ± |  |  |  | ± |  |  |  | ± |  |
| Ammonium (NH4+) |  | 0.3030 | ± | 0.2229 |  | 0.0738 | ± | 0.0965 |  | 0.3131 | ± | 0.2835 |  | 0.0410 | ± | 0.1756 |  | 0.2212 | ± | 0.1492 |  | 0.1287 | ± | 0.2004 |  | 0.1250 | ± | 0.2179 |
| Soluble Sodium (NA+) |  | 0.1278 | ± | 0.0652 |  | 0.1959 | ± | 0.2110 |  | 0.1166 | ± | 0.0479 |  | 0.1667 | ± | 0.0735 |  | 0.1674 | ± | 0.2478 |  | 0.2554 | ± | 0.2388 |  | 0.4150 | ± | 0.5012 |
| Soluble Potassium (K+) |  | 0.1003 | ± | 0.0426 |  | 0.5407 | ± | 1.1261 |  | 0.1129 | ± | 0.0554 |  | 0.2689 | ± | 0.1191 |  | 0.4778 | ± | 1.2885 |  | 0.7961 | ± | 1.2537 |  | 0.6300 | ± | 0.9005 |
| Organic Carbon (OC) |  | 5.1404 | ± | 3.9169 |  | 7.7118 | ± | 5.7604 |  | 5.8783 | ± | 3.1689 |  | 14.3364 | ± | 8.6581 |  | 5.2122 | ± | 7.4936 |  | 10.2941 | ± | 5.3210 |  | 9.8325 | ± | 8.9002 |
| Elemental Carbon (EC) |  | 0.7319 | ± | 0.8206 |  | 0.2427 | ± | 0.4471 |  | 0.7142 | ± | 0.8839 |  | 1.9158 | ± | 1.2907 |  | 0.2811 | ± | 0.5188 |  | 0.6930 | ± | 0.7184 |  | 0.8075 | ± | 0.8413 |
| Total Carbon (TC) |  | 5.8722 | ± | 4.7351 |  | 7.9545 | ± | 5.7526 |  | 6.5925 | ± | 3.9902 |  | 16.2522 | ± | 9.9331 |  | 5.4932 | ± | 7.5183 |  | 10.9871 | ± | 5.0670 |  | 10.6400 | ± | 9.5544 |
| Sodium (Na) |  | 0.1596 | ± | 0.0722 |  |  | ± |  |  | 0.2573 | ± | 0.1372 |  |  | ± |  |  | 0.2151 | ± | 0.1608 |  |  | ± |  |  |  | ± |  |
| Magnesium (Mg) |  | 0.7901 | ± | 0.1068 |  |  | ± |  |  | 0.7589 | ± | 0.0403 |  |  | ± |  |  | 1.0435 | ± | 0.5089 |  |  | ± |  |  |  | ± |  |
| Aluminum (Al) |  | 10.7048 | ± | 3.2190 |  | 9.8345 | ± | 3.1254 |  | 10.2350 | ± | 3.0895 |  | 9.9696 | ± | 2.9544 |  | 10.8591 | ± | 3.6945 |  | 7.6744 | ± | 2.5296 |  | 7.8225 | ± | 3.7028 |
| Silicon (Si) |  | 29.8763 | ± | 9.4845 |  | 26.7123 | ± | 8.4305 |  | 30.2927 | ± | 9.6339 |  | 26.7660 | ± | 9.6262 |  | 30.5721 | ± | 10.0417 |  | 22.0516 | ± | 5.2890 |  | 19.1875 | ± | 8.1462 |
| Phosphorus (P) |  | 0.2682 | ± | 0.3211 |  |  | ± |  |  | 0.2918 | ± | 0.3003 |  |  | ± |  |  | 0.6821 | ± | 1.9578 |  |  | ± |  |  |  | ± |  |
| Sulfur (S) |  | 0.3055 | ± | 0.1724 |  | 0.2991 | ± | 0.1469 |  | 0.5187 | ± | 0.3645 |  | 0.4719 | ± | 0.3297 |  | 0.2445 | ± | 0.1946 |  | 0.4131 | ± | 0.1415 |  | 0.3400 | ± | 0.3281 |
| Chlorine (Cl) |  | 0.0670 | ± | 0.1161 |  | 0.2988 | ± | 0.4772 |  | 0.0681 | ± | 0.1152 |  | 0.1123 | ± | 0.0795 |  | 0.1878 | ± | 0.5772 |  | 0.4613 | ± | 0.4827 |  | 0.2500 | ± | 0.2609 |
| Potassium (K) |  | 2.6354 | ± | 0.5181 |  | 3.1668 | ± | 1.3894 |  | 2.9830 | ± | 0.5810 |  | 2.2958 | ± | 0.9203 |  | 3.0996 | ± | 1.5112 |  | 3.2636 | ± | 1.5926 |  | 2.7325 | ± | 0.4043 |
| Calcium (Ca) |  | 2.6988 | ± | 0.7989 |  | 4.5415 | ± | 2.6815 |  | 3.0631 | ± | 0.7204 |  | 3.0144 | ± | 0.6659 |  | 2.7038 | ± | 2.0238 |  | 5.5362 | ± | 3.0295 |  | 3.4375 | ± | 0.4205 |
| Titanium (Ti) |  | 0.4691 | ± | 0.1498 |  | 0.5657 | ± | 0.2108 |  | 0.4657 | ± | 0.1519 |  | 0.4849 | ± | 0.0528 |  | 0.4883 | ± | 0.1723 |  | 0.4400 | ± | 0.2448 |  | 0.6275 | ± | 0.2794 |
| Vanadium (V) |  | 0.0069 | ± | 0.0265 |  | 0.0253 | ± | 0.0274 |  | 0.0054 | ± | 0.0283 |  | 0.0237 | ± | 0.0219 |  | 0.0111 | ± | 0.0294 |  | 0.0187 | ± | 0.0224 |  | 0.0325 | ± | 0.0150 |
| Chromium (Cr) |  | 0.0028 | ± | 0.0080 |  | 0.0147 | ± | 0.0134 |  | 0.0012 | ± | 0.0086 |  | 0.0220 | ± | 0.0136 |  | 0.0036 | ± | 0.0090 |  | 0.0131 | ± | 0.0144 |  | 0.0250 | ± | 0.0100 |
| Manganese (Mn) |  | 0.0773 | ± | 0.0043 |  | 0.1372 | ± | 0.0716 |  | 0.0866 | ± | 0.0152 |  | 0.1072 | ± | 0.0179 |  | 0.0765 | ± | 0.0135 |  | 0.1078 | ± | 0.0824 |  | 0.1075 | ± | 0.0330 |
| Iron (Fe) |  | 5.3765 | ± | 0.9478 |  | 6.4555 | ± | 2.4510 |  | 5.0458 | ± | 1.1553 |  | 5.3032 | ± | 0.5787 |  | 5.3319 | ± | 1.6103 |  | 5.0877 | ± | 2.8375 |  | 6.1575 | ± | 2.7884 |
| Cobalt (Co) |  | 0.0017 | ± | 0.0846 |  |  | ± |  |  | 0.0021 | ± | 0.0799 |  |  | ± |  |  | 0.0024 | ± | 0.0791 |  |  | ± |  |  |  | ± |  |
| Nickel (Ni) |  | 0.0033 | ± | 0.0037 |  | 0.0057 | ± | 0.0049 |  | 0.0012 | ± | 0.0024 |  | 0.0077 | ± | 0.0046 |  | 0.0035 | ± | 0.0046 |  | 0.0058 | ± | 0.0049 |  | 0.0075 | ± | 0.0050 |
| Copper (Cu) |  | 0.0183 | ± | 0.0074 |  | 0.0109 | ± | 0.0051 |  | 0.0168 | ± | 0.0076 |  | 0.0180 | ± | 0.0042 |  | 0.0107 | ± | 0.0056 |  | 0.0146 | ± | 0.0072 |  | 0.0100 | ± | 0.0000 |
| Zinc (Zn) |  | 0.0887 | ± | 0.0544 |  | 0.0719 | ± | 0.0403 |  | 0.1225 | ± | 0.0935 |  | 0.1385 | ± | 0.0823 |  | 0.0713 | ± | 0.0501 |  | 0.0665 | ± | 0.0522 |  | 0.0950 | ± | 0.0819 |
| Gallium (Ga) |  | 0.0012 | ± | 0.0017 |  |  | ± |  |  | 0.0010 | ± | 0.0019 |  |  | ± |  |  | 0.0008 | ± | 0.0020 |  |  | ± |  |  |  | ± |  |
| Arsenic (As) |  | 0.0018 | ± | 0.0023 |  |  | ± |  |  | 0.0015 | ± | 0.0027 |  |  | ± |  |  | 0.0016 | ± | 0.0025 |  |  | ± |  |  |  | ± |  |
| Selenium (Se) |  | 0.0002 | ± | 0.0009 |  |  | ± |  |  | 0.0002 | ± | 0.0011 |  |  | ± |  |  | 0.0002 | ± | 0.0011 |  |  | ± |  |  |  | ± |  |
| Bromine (Br) |  | 0.0014 | ± | 0.0010 |  | 0.0051 | ± | 0.0040 |  | 0.0014 | ± | 0.0010 |  | 0.0073 | ± | 0.0046 |  | 0.0014 | ± | 0.0018 |  | 0.0042 | ± | 0.0043 |  | 0.0000 | ± | 0.0000 |
| Rubidium (Rb) |  | 0.0124 | ± | 0.0034 |  |  | ± |  |  | 0.0140 | ± | 0.0029 |  |  | ± |  |  | 0.0131 | ± | 0.0037 |  |  | ± |  |  |  | ± |  |
| Strontium (Sr) |  | 0.0274 | ± | 0.0045 |  |  | ± |  |  | 0.0314 | ± | 0.0028 |  |  | ± |  |  | 0.0254 | ± | 0.0099 |  |  | ± |  |  |  | ± |  |
| Yttrium (Y) |  | 0.0027 | ± | 0.0012 |  |  | ± |  |  | 0.0026 | ± | 0.0012 |  |  | ± |  |  | 0.0030 | ± | 0.0011 |  |  | ± |  |  |  | ± |  |
| Zirconium (Zr) |  | 0.0142 | ± | 0.0039 |  |  | ± |  |  | 0.0144 | ± | 0.0037 |  |  | ± |  |  | 0.0105 | ± | 0.0037 |  |  | ± |  |  |  | ± |  |
| Molybdenum (Mo) |  | 0.0004 | ± | 0.0024 |  |  | ± |  |  | 0.0004 | ± | 0.0028 |  |  | ± |  |  | 0.0006 | ± | 0.0028 |  |  | ± |  |  |  | ± |  |
| Palladium (Pd) |  | 0.0005 | ± | 0.0146 |  |  | ± |  |  | 0.0001 | ± | 0.0168 |  |  | ± |  |  | 0.0001 | ± | 0.0169 |  |  | ± |  |  |  | ± |  |
| Silver (Ag) |  | 0.0001 | ± | 0.0171 |  |  | ± |  |  | 0.0002 | ± | 0.0196 |  |  | ± |  |  | 0.0000 | ± | 0.0199 |  |  | ± |  |  |  | ± |  |
| Cadmium (Cd) |  | 0.0006 | ± | 0.0181 |  |  | ± |  |  | 0.0002 | ± | 0.0208 |  |  | ± |  |  | 0.0002 | ± | 0.0210 |  |  | ± |  |  |  | ± |  |
| Indium (In) |  | 0.0001 | ± | 0.0203 |  |  | ± |  |  | 0.0000 | ± | 0.0234 |  |  | ± |  |  | 0.0001 | ± | 0.0236 |  |  | ± |  |  |  | ± |  |
| Tin (Sn) |  | 0.0057 | ± | 0.0256 |  |  | ± |  |  | 0.0067 | ± | 0.0294 |  |  | ± |  |  | 0.0012 | ± | 0.0297 |  |  | ± |  |  |  | ± |  |
| Antimony (Sb) |  | 0.0087 | ± | 0.0297 |  |  | ± |  |  | 0.0112 | ± | 0.0341 |  |  | ± |  |  | 0.0022 | ± | 0.0345 |  |  | ± |  |  |  | ± |  |
| Barium (Ba) |  | 0.1106 | ± | 0.0778 |  |  | ± |  |  | 0.1123 | ± | 0.0912 |  |  | ± |  |  | 0.0656 | ± | 0.1136 |  |  | ± |  |  |  | ± |  |
| Lanthanum (La) |  | 0.0149 | ± | 0.1406 |  |  | ± |  |  | 0.0139 | ± | 0.1619 |  |  | ± |  |  | 0.0188 | ± | 0.1645 |  |  | ± |  |  |  | ± |  |
| Gold (Au) |  | 0.0002 | ± | 0.0045 |  |  | ± |  |  | 0.0000 | ± | 0.0060 |  |  | ± |  |  | 0.0004 | ± | 0.0043 |  |  | ± |  |  |  | ± |  |
| Mercury (Hg) |  | 0.0006 | ± | 0.0021 |  |  | ± |  |  | 0.0008 | ± | 0.0024 |  |  | ± |  |  | 0.0007 | ± | 0.0024 |  |  | ± |  |  |  | ± |  |
| Thallium (Tl) |  | 0.0003 | ± | 0.0020 |  |  | ± |  |  | 0.0005 | ± | 0.0023 |  |  | ± |  |  | 0.0005 | ± | 0.0023 |  |  | ± |  |  |  | ± |  |
| Lead (Pb) |  | 0.0090 | ± | 0.0065 |  | 0.0848 | ± | 0.2866 |  | 0.0101 | ± | 0.0053 |  | 0.1840 | ± | 0.1267 |  | 0.0060 | ± | 0.0064 |  | 0.0874 | ± | 0.3204 |  | 0.1175 | ± | 0.1493 |
| Uranium (U) |  | 0.0014 | ± | 0.0022 |  |  | ± |  |  | 0.0018 | ± | 0.0027 |  |  | ± |  |  | 0.0021 | ± | 0.0025 |  |  | ± |  |  |  | ± |  |

Table 2. Other Categories of Source Profiles for CMB Modeling

| Category |  | Motor Vehicle Exhaust |  | Tire and Break Wear |  | Vegetative Burning |  | Vegetative Burning |  | Ammonium Nitrate |  | Ammonium Sulfate |  | Organic Carbon |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mnemonics |  | CAMV |  | TireBrke |  | WBOakEuc |  | AgBWheat |  | AMNIT |  | AMSUL |  | OC |
| Chloride (Cl-) |  | 0.3101 | ± | 0.5964 |  | 0.1360 | ± | 0.0793 |  | 1.9019 | ± | 2.3403 |  | 8.2360 | ± | 1.3595 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Nitrate (NO3-) |  | 0.2516 | ± | 0.4826 |  | 0.7310 | ± | 0.4922 |  | 0.5742 | ± | 0.0661 |  | 0.1647 | ± | 0.0175 |  | 77.5000 | ± | 7.7500 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Phosphate (PO42-) |  |  | ± |  |  |  | ± |  |  |  | ± |  |  |  | ± |  |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Sulfate (SO42-) |  | 0.7585 | ± | 0.8304 |  | 1.7765 | ± | 0.8686 |  | 1.3041 | ± | 0.8318 |  | 0.4383 | ± | 0.0422 |  | 0.0000 | ± | 0.0000 |  | 72.7000 | ± | 7.2700 |  | 0.0000 | ± | 0.0000 |
| Ammonia (NH3) |  |  | ± |  |  |  | ± |  |  | 2.0401 | ± | 1.7908 |  | 0.2719 | ± | 0.0350 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Ammonium (NH4+) |  | 0.8077 | ± | 0.9702 |  | 0.5090 | ± | 0.3107 |  | 0.5832 | ± | 0.4667 |  | 0.5859 | ± | 0.0440 |  | 22.5500 | ± | 2.2550 |  | 27.3000 | ± | 2.7300 |  | 0.0000 | ± | 0.0000 |
| Soluble Sodium (NA+) |  |  | ± |  |  | 0.3039 | ± | 0.1799 |  | 0.3833 | ± | 0.1520 |  | 0.5393 | ± | 0.0403 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Soluble Potassium (K+) |  |  | ± |  |  | 0.1346 | ± | 0.0710 |  | 2.8911 | ± | 0.4497 |  | 6.7935 | ± | 0.4962 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Organic Carbon (OC) |  | 39.9006 | ± | 21.6042 |  | 30.4125 | ± | 9.2310 |  | 59.5824 | ± | 4.7535 |  | 57.0282 | ± | 4.5365 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 100.0000 | ± | 10.0000 |
| Elemental Carbon (EC) |  | 41.2797 | ± | 24.8290 |  | 7.3851 | ± | 2.2577 |  | 5.2016 | ± | 1.1170 |  | 10.3141 | ± | 0.8469 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Total Carbon (TC) |  | 81.3235 | ± | 29.8023 |  | 37.7975 | ± | 11.4887 |  | 64.7840 | ± | 5.1338 |  | 67.3449 | ± | 5.3233 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 100.0000 | ± | 10.0000 |
| Sodium (Na) |  | 0.0934 | ± | 0.7803 |  | 0.0000 | ± | 0.1759 |  | 0.8753 | ± | 0.5740 |  | 0.0000 | ± | 0.5189 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Magnesium (Mg) |  | 0.2825 | ± | 0.3212 |  | 0.4510 | ± | 0.2425 |  | 0.0223 | ± | 0.0679 |  | 0.0284 | ± | 0.0597 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Aluminum (Al) |  | 0.3568 | ± | 0.5629 |  | 1.2129 | ± | 0.8138 |  | 0.0733 | ± | 0.0489 |  | 0.0739 | ± | 0.0087 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Silicon (Si) |  | 2.3582 | ± | 2.3385 |  | 1.5450 | ± | 0.7461 |  | 0.2201 | ± | 0.0953 |  | 0.1287 | ± | 0.0098 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Phosphorus (P) |  | 0.5385 | ± | 0.3709 |  | 0.0024 | ± | 0.0172 |  | 0.0000 | ± | 0.0076 |  | 0.0017 | ± | 0.0059 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Sulfur (S) |  | 0.5360 | ± | 0.1941 |  | 1.1960 | ± | 0.3258 |  | 0.4121 | ± | 0.3260 |  | 0.1337 | ± | 0.0098 |  | 0.0000 | ± | 0.0000 |  | 24.2700 | ± | 2.4270 |  | 0.0000 | ± | 0.0000 |
| Chlorine (Cl) |  | 0.3220 | ± | 0.5331 |  | 0.0724 | ± | 0.0307 |  | 1.7220 | ± | 2.0160 |  | 6.1585 | ± | 0.4360 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Potassium (K) |  | 0.0226 | ± | 0.1231 |  | 0.2680 | ± | 0.1526 |  | 2.8621 | ± | 0.9341 |  | 5.4967 | ± | 0.3891 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Calcium (Ca) |  | 0.8183 | ± | 0.5229 |  | 0.7712 | ± | 0.4376 |  | 0.1484 | ± | 0.1025 |  | 0.1031 | ± | 0.0321 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Titanium (Ti) |  | 0.0121 | ± | 0.4305 |  | 0.0929 | ± | 0.1499 |  | 0.0067 | ± | 0.0236 |  | 0.0053 | ± | 0.0130 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Vanadium (V) |  | 0.0055 | ± | 0.2707 |  | 0.0000 | ± | 0.0667 |  | 0.0002 | ± | 0.0095 |  | 0.0000 | ± | 0.0076 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Chromium (Cr) |  | 0.0071 | ± | 0.0475 |  | 0.0821 | ± | 0.0308 |  | 0.0021 | ± | 0.0030 |  | 0.0000 | ± | 0.0022 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Manganese (Mn) |  | 0.0021 | ± | 0.0266 |  | 0.3417 | ± | 0.1766 |  | 0.0060 | ± | 0.0035 |  | 0.0024 | ± | 0.0004 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Iron (Fe) |  | 2.0565 | ± | 1.7735 |  | 43.3272 | ± | 19.3830 |  | 0.0930 | ± | 0.0593 |  | 0.0687 | ± | 0.0049 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Cobalt (Co) |  | 0.0000 | ± | 0.0352 |  | 0.0181 | ± | 0.3796 |  | 0.0002 | ± | 0.0018 |  | 0.0000 | ± | 0.0013 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Nickel (Ni) |  | 0.0170 | ± | 0.0322 |  | 0.0000 | ± | 0.0088 |  | 0.0006 | ± | 0.0008 |  | 0.0001 | ± | 0.0008 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Copper (Cu) |  | 0.0315 | ± | 0.0292 |  | 0.4849 | ± | 0.2919 |  | 0.0064 | ± | 0.0016 |  | 1.0241 | ± | 0.0725 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Zinc (Zn) |  | 0.7860 | ± | 0.6524 |  | 1.4708 | ± | 1.0257 |  | 0.0426 | ± | 0.0180 |  | 0.0139 | ± | 0.0013 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Gallium (Ga) |  | 0.0000 | ± | 0.0002 |  | 0.0025 | ± | 0.0046 |  | 0.0010 | ± | 0.0018 |  | 0.0000 | ± | 0.0010 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Arsenic (As) |  | 0.0000 | ± | 0.0033 |  | 0.0000 | ± | 0.0068 |  | 0.0005 | ± | 0.0018 |  | 0.0006 | ± | 0.0008 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Selenium (Se) |  | 0.0000 | ± | 0.0000 |  | 0.0003 | ± | 0.0025 |  | 0.0002 | ± | 0.0007 |  | 0.0001 | ± | 0.0004 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Bromine (Br) |  | 0.0002 | ± | 0.0005 |  | 0.0069 | ± | 0.0045 |  | 0.0046 | ± | 0.0015 |  | 0.0337 | ± | 0.0024 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Rubidium (Rb) |  | 0.0000 | ± | 0.0000 |  | 0.0067 | ± | 0.0041 |  | 0.0057 | ± | 0.0006 |  | 0.0003 | ± | 0.0013 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Strontium (Sr) |  | 0.0000 | ± | 0.0000 |  | 0.5430 | ± | 0.2760 |  | 0.0013 | ± | 0.0004 |  | 0.0015 | ± | 0.0002 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Yttrium (Y) |  | 0.0000 | ± | 0.0001 |  | 0.0003 | ± | 0.0028 |  | 0.0007 | ± | 0.0015 |  | 0.0003 | ± | 0.0008 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Zirconium (Zr) |  | 0.0000 | ± | 0.0009 |  | 0.0053 | ± | 0.0136 |  | 0.0000 | ± | 0.0017 |  | 0.0015 | ± | 0.0003 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Molybdenum (Mo) |  | 0.0000 | ± | 0.0009 |  | 0.0026 | ± | 0.0059 |  | 0.0000 | ± | 0.0029 |  | 0.0000 | ± | 0.0016 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Palladium (Pd) |  | 0.0000 | ± | 0.2190 |  | 0.0004 | ± | 0.0195 |  | 0.0007 | ± | 0.0036 |  | 0.0000 | ± | 0.0018 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Silver (Ag) |  | 0.0000 | ± | 0.2855 |  | 0.0093 | ± | 0.0236 |  | 0.0022 | ± | 0.0046 |  | 0.0011 | ± | 0.0021 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Cadmium (Cd) |  | 0.0000 | ± | 0.2856 |  | 0.0019 | ± | 0.0247 |  | 0.0018 | ± | 0.0047 |  | 0.0014 | ± | 0.0022 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Indium (In) |  | 0.0077 | ± | 0.2857 |  | 0.0114 | ± | 0.0267 |  | 0.0009 | ± | 0.0059 |  | 0.0000 | ± | 0.0030 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Tin (Sn) |  | 0.0002 | ± | 0.4651 |  | 0.0346 | ± | 0.0326 |  | 0.0000 | ± | 0.0082 |  | 0.0028 | ± | 0.0042 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Antimony (Sb) |  | 0.0052 | ± | 0.6450 |  | 0.0420 | ± | 0.0397 |  | 0.0006 | ± | 0.0097 |  | 0.0045 | ± | 0.0050 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Barium (Ba) |  | 0.1010 | ± | 1.2963 |  | 1.7800 | ± | 1.2578 |  | 0.0192 | ± | 0.0465 |  | 0.0000 | ± | 0.0234 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Lanthanum (La) |  | 0.0648 | ± | 1.5900 |  | 0.0000 | ± | 0.1839 |  | 0.0000 | ± | 0.0614 |  | 0.0163 | ± | 0.0317 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Gold (Au) |  | 0.0000 | ± | 0.6031 |  | 0.0026 | ± | 0.0386 |  | 0.0008 | ± | 0.0029 |  | 0.0000 | ± | 0.0013 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Mercury (Hg) |  | 0.0000 | ± | 0.0110 |  | 0.0000 | ± | 0.0061 |  | 0.0002 | ± | 0.0015 |  | 0.0000 | ± | 0.0008 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Thallium (Tl) |  | 0.0000 | ± | 0.0014 |  | 0.0049 | ± | 0.0055 |  | 0.0004 | ± | 0.0016 |  | 0.0000 | ± | 0.0008 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Lead (Pb) |  | 0.0292 | ± | 0.0449 |  | 0.0504 | ± | 0.0197 |  | 0.0046 | ± | 0.0025 |  | 0.0000 | ± | 0.0014 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |
| Uranium (U) |  | 0.0000 | ± | 0.0009 |  | 0.0000 | ± | 0.0055 |  | 0.0008 | ± | 0.0027 |  | 0.0012 | ± | 0.0015 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |  | 0.0000 | ± | 0.0000 |

## Geological Material

Geological material is a significant component of PM10 in the San Joaquin Valley.  It comes from a variety of sources, including roads (paved and unpaved), agricultural operations such as land preparation and harvesting, construction, and soil erosion.  The central California Fugitive Dust Characterization Study aquired 47 samples from 37 areas including: 1) paved road dust from urban and rural areas, 2) unpaved road dust, 3) agricultural soil from five crop fields (almond, cotton, grape, safflower, and tomato), 4) soil from dairy and feedlot, 5) salt buildup deposits from irrigation canal drainages, and 6) building construction/earthmoving soil.  Table 3 includes a summary of collected samples. Individual sample profiles, collected as part of the above mentioned project and from other library sources, were averaged to create composite profiles that best represents fugitive dust sources at each exceedance site in the San Joaquin Valley.  Table 4 lists all profiles included in the composites for each of the episodes and Table 5 lists profiles included in the composites created for modeling annual average concentrations.

Table 3.  Summary of Geological Samples Collected
in the San Joaquin Valley as part of the TSS12 Project

| Source Type | Subtype | County | Sample ID | Latitude | Longitude | Soil Classification |
| --- | --- | --- | --- | --- | --- | --- |
| Agricultural Soil | Cotton | Fresno | FDCOT1A | 36º34'30" | 120º05'12" | Chino Fine Sandy Loam |
|  |  |  | FDCOT1C | 36º34'43" | 120º05'09" | Chino Fine Sandy Loam |
|  |  |  | FDCOT2A | 36º15'28" | 119º59'45" | Cerini Clay Loam |
|  |  |  | FDCOT2B | 36º15'44" | 119º59'47" | Cerini Clay Loam |
|  |  |  | FDCOT2C | 36º15'45" | 120º00'14" | Cerini Clay Loam |
|  |  | Kern | FDCOT3A | 35º12'27" | 119º16'42" | Copus Silty Clay |
|  |  |  | FDCOT3B | 35º12'05" | 119º17'14" | Copus Silty Clay |
|  |  |  | FDCOT3C | 35º12'08" | 119º16'20" | Copus Silty Clay |
|  |  |  | FDCOT4A | 35º08'59" | 119º01'22" | Lokern Clay |
|  |  | Kings | FDCOT5A | 36º08'05" | 119º58'56" | Westhaven Loam |
|  | Tomato | Fresno | FDTOM1A | 36º47'17" | 120º26'24" | Panoche Silty Clay |
|  |  |  | FDTOM1B | 36º47'17" | 120º26'00" | Panoche Silty Clay |
|  |  |  | FDTOM2A | 36º08'59" | 119º30'27" | N/A |
|  |  |  | FDTOM3A | 36º08'59" | 119º30'27" | N/A |
|  | Almonds | Kern | FDALM1A | 35º29'52" | 119º09'31" | Driver Coarse Sandy Loam |
|  |  |  | FDALM1B | 35º29'47" | 119º09'31" | Driver Coarse Sandy Loam |
|  |  |  | FDALM1C | 35º29'40" | 119º09'12" | Driver Coarse Sandy Loam |
|  |  | Fresno | FDALM2 | 36º35'28" | 120º03'50" | N/A |
|  |  | Kings | FDALM3 | 35º39'27" | 119º53'39" | Kimberlina Fine Sandy Loam |
|  |  | Madera | FDALM4 | 37º20'47" | 120º43'25" | Dinuba Sandy Loam |
|  | Grapes | Fresno | FDGRA1 | 36º38'51" | 119º49'05" | Hesperia Fine Sandy Loam |
|  |  | Madera | FDGRA2 | 36º53'03" | 120º04'03" | N/A |
|  | Safflower | Kings | FDSAF1 | 35º58'43" | 119º39'41" | Tulare Clay |
|  |  | Kern | FDSAF2 | 35º11'37" | 119º15'39" | Zalvidea Sandy Clay Loam |
|  |  |  | FDSAF3 | 35º09'09" | 119º01'22" | Oldriver Loam |
| Animal Husbandry | Dairy | Kings | FDCTD1 | 36º07'13" | 119º31'13" | Organic |
|  |  | Fresno | FDCTD2 | 35º57'41" | 119º39'08" | Organic |
|  | Feedlot | Kern | FDCTF1 | 35º30'02" | 119º06'30" | Organic |
|  |  | Fresno | FDCTF2 | 36º15'10" | 120º15'53" | Organic |
| Paved Road Dust | Urban | Kern | FDPVR1 | 36º18'09" | 120º15'54" | Paved Road |
|  | Rural | Kern | FDPVR3 | 35º36'07" | 119º18'41" | Paved Road |
|  |  | Tulare | FDPVR4 | 36º08'59" | 119º30'27" | Paved Road |
| Unpaved Road Dust | Agricultural | Fresno | FDUPR1 | 36º34'45" | 120º03'05" | Unpaved Road |
|  |  | Kern | FDUPR3 | 35º12'08" | 119º16'22" | Unpaved Road |
|  | Public /Residential | Kings | FDUPR4 | 36º05'51" | 119º35'09" | Unpaved Road |
|  |  |  | FDUPR5 | 35º36'52" | 119º41'35" | Unpaved Road |
|  |  |  | FDUPR6 | 36º00'34" | 119º58'03" | Unpaved Road |
|  | Staging Area | Kings | FDSTA1 | 36º08'02" | 119º58'56" | Unpaved Road |
| Disturbed Soil | Disturbed Land Salt Buildup | Kings | FDDIS1 | 35º50'20" | 119º39'44" | Disturbed Land |
|  |  | Kern | FDDIS2 | 35º09'05" | 119º01'19" | Disturbed Land |
|  | Construction/earthmoving | Fresno | FDCON1 | 36º47'07" | 120º03'40" | Construction |
|  |  | Madera | FDCON2 | 36º56'27" | 120º03'26" | Construction |

Table 4. Episode Specific Geological Source Profiles

| Composite Profile ID | Sample ID | % Weight | Applicable Month/Area |
| --- | --- | --- | --- |
| DUST | Generic composite profile, which is an average of all profiles listed in Table 2. |
| FDBACNOV | SOIL31 | 10 | November / Bakersfield |
|  | FDCOT | 10 |  |
|  | SOIL13 | 20 |  |
|  | FDCTF | 15 |  |
|  | FDPVR1 | 45 |  |
| FDBACJAN | SOIL13 | 30 | January / Bakersfield |
|  | FDPVR1 | 70 |  |
| FDOIL | SOIL31 | 10 | January / Oildale |
|  | FDPVR | 20 |  |
|  | SOIL13 | 40 |  |
|  | FDCTF | 15 |  |
|  | FDUPR | 15 |  |
| FDCOPOCT | FDCOT4 | 30 | October / Corcoran |
|  | FDPVR3 | 35 |  |
|  | FDUPR | 20 |  |
|  | FDCTF | 15 |  |
| FDCOPDEC | FDCOT4 | 20 | December / Corcoran |
|  | FDPVR3 | 50 |  |
|  | FDUPR | 20 |  |
|  | FDCTF | 10 |  |
| FDCOPJAN | FDCOT4 | 10 | January / Corcoran and Hanford. |
|  | FDPVR3 | 60 |  |
|  | FDUPR | 20 |  |
|  | FDCTF | 10 |  |
| FDTUR | FDALM | 1/3 *100 | October / Turlock |
|  | FDPVR1 | 1/3 *100 |  |
|  | FDPVR3 | 1/3 *100 |  |
| FDM14 | FDTOM | 1/3 *100 | January / Modesto |
|  | FDPVR1 | 1/3 *100 |  |
|  | FDPVR3 | 1/3 *100 |  |
| FDHANNOV | The same as FDCOPOCT |  |
| FDHANDEC | The same as FDCOPDEC |  |
| FDHANJAN | The same as FDCOPJAN |  |
| FDFREOCT | FDALM | 10 | October / Fresno-Drummond |
|  | FDGRA1 | 25 |  |
|  | SOIL03 | 65 |  |
| FDFREDEC | FDTOM1 | 20 | December and January / Clovis, Fresno-1st, and Fresno-Drummond |
|  | SOIL03 | 80 |  |

Table 5. Annual Geological Source Profiles

| Composite Profile ID | Sample ID | % Weight | Applicable Month/Area |
| --- | --- | --- | --- |
| FDKERANN | SOIL31 | 25 | Annual / Kern County |
|  | FDPVR1 | 25 |  |
|  | FDCTF | 25 |  |
|  | SOIL13 | 25 |  |
| FDHANANN | FDUPR | 10 | Annual / Hanford |
|  | FDCTF | 15 |  |
|  | FDCOT5 | 30 |  |
|  | FDPVR3 | 45 |  |
| FDVCSANN | SOIL04 | 25 | Annual / Visalia |
|  | SOIL07 | 25 |  |
|  | SOIL08 | 25 |  |
|  | VIDAIC | 25 |  |
| FDFREANN | SOIL03 | 70 | Annual / Fresno |
|  | FDALM | 10 |  |
|  | FDGRA1 | 10 |  |
|  | FDTOM1 | 10 |  |

## Motor Vehicle

The following documents summarize samples collected to represent motor vehicle fleet in California:

- “Measurement of Primary Particulate Matter Emissions from Light-Duty Motor Vehicles”, CRC Project No. E-24-2, Center for Environmental Research and Technology, College of Engineering, University of California, Riverside, December 1998.

- “Characterization of Particulate Emissions from Gasoline Fueled Vehicles”, California Air Resources Board, Contract 94-319, September 1998.

Vehicles were tested over the FTP Cycle as part of the CRC project and over the Unified Cycle as part of the ARB project.  Elemental and organic carbon were the primary constituents for the particulate matter.  On average, organic carbon composed a larger fraction of the total carbon for the gasoline vehicles, while elemental carbon represented a larger fraction of the total carbon for the diesel vehicles.  There was considerable variability from vehicle to vehicle, however, with some gasoline vehicles heaving higher percentages of elemental carbon that organic carbon and some diesel vehicles having higher percentages of organic carbon than elemental carbon (Table 6).  The contribution of organic carbon was generally larger for the older, higher emitting vehicles.

In order to develop a source profile useful for receptor modeling, individual sample profiles were averaged to represent motor vehicle emissions for the San Joaquin Valley.  The individual sample profiles were composited by the source type and sub-type using the Department of Motor Vehicles and EMFAC2002 version 2.2 breakdown of the motor vehicle fleet.  The breakdown numbers for the fleet are presented in Table 7.

Listed below are the different levels of subset grouping that needed to be created in order to represent an average motor vehicle fleet:

- Cars and trucks

- Year bin (91-00, 81-90, and 65-80)

- Exhaust control technology (Non-cat, cat, and diesel).

Table 8 shows variations in carbon as a weight percent of PM10 mass between groups and subgroups.

Table 6.  Elemental and Organic Carbon for Gasoline and Diesel Vehicles
(Weight Percent Mass)

| Vehicle Type | Year Bin |  | Year, Make, and Model | OC | EC | TC |
| --- | --- | --- | --- | --- | --- | --- |
| Truck | 91-00 | Catalyst | 1997 Ford Windstar | 6 | ± | 2 | 109 | ± | 16 | 115 | ± | 16 |
| Car | 91-00 | Catalyst | 1994 Dodge Spirit | 51 | ± | 8 | 58 | ± | 6 | 110 | ± | 13 |
| Car | 91-00 | Catalyst | 1994 Dodge Shadow | 18 | ± | 6 | 22 | ± | 2 | 40 | ± | 8 |
| Truck | 91-00 | Catalyst | 1994 Dodge Caravan | 22 | ± | 4 | 50 | ± | 5 | 72 | ± | 9 |
| Truck | 91-00 | Catalyst | 1994 Chevrolet C1500 Suburban | 11 | ± | 3 | 23 | ± | 3 | 34 | ± | 5 |
| Truck | 91-00 | Catalyst | 1992 Toyota Pick-up | 52 | ± | 9 | 70 | ± | 10 | 122 | ± | 18 |
| Truck | 91-00 | Catalyst | 1992 Dodge Dakota LE | 21 | ± | 4 | 58 | ± | 9 | 79 | ± | 12 |
| Car | 91-00 | Catalyst | 1991 Toyota Tercel | 39 | ± | 8 | 53 | ± | 8 | 91 | ± | 15 |
| Truck | 91-00 | Catalyst | 1991 Toyota Pick-Up | 13 | ± | 4 | 81 | ± | 12 | 94 | ± | 14 |
| Truck | 91-00 | Catalyst | 1991 Pontiac Transport | 82 | ± | 11 | 6 | ± | 1 | 88 | ± | 13 |
| Car | 81-90 | Catalyst | 1990 Nissan Stanza | 20 | ± | 3 | 46 | ± | 4 | 67 | ± | 7 |
| Car | 81-90 | Catalyst | 1990 Nissan Sentra | 13 | ± | 4 | 92 | ± | 14 | 104 | ± | 16 |
| Car | 81-90 | Catalyst | 1990 Honda Accord EX | 61 | ± | 9 | 16 | ± | 2 | 77 | ± | 10 |
| Car | 81-90 | Catalyst | 1990 Ford Tempo | 15 | ± | 3 | 8 | ± | 1 | 24 | ± | 4 |
| Truck | 81-90 | Catalyst | 1990 Dodge Ram 250 | 34 | ± | 5 | 4 | ± | 1 | 38 | ± | 5 |
| Car | 81-90 | Catalyst | 1989 Toyota Celica | 6 | ± | 7 | 29 | ± | 3 | 36 | ± | 8 |
| Car | 81-90 | Catalyst | 1989 Hyundai Excel GL | 57 | ± | 8 | 1 | ± | 0 | 58 | ± | 8 |
| Truck | 81-90 | Catalyst | 1989 GMC Sierra1500 | 112 | ± | 17 | 7 | ± | 1 | 119 | ± | 18 |
| Truck | 81-90 | Catalyst | 1989 Dodge Caravan | 87 | ± | 12 | 3 | ± | 0 | 90 | ± | 12 |
| Car | 81-90 | Catalyst | 1988 Mazda MX-6 | 26 | ± | 4 | 51 | ± | 8 | 77 | ± | 11 |
| Truck | 81-90 | Catalyst | 1988 Dodge Ram Royal | 57 | ± | 9 | 39 | ± | 6 | 97 | ± | 15 |
| Truck | 81-90 | Catalyst | 1988 Dodge Caravan | 88 | ± | 12 | 7 | ± | 1 | 95 | ± | 13 |
| Car | 81-90 | Catalyst | 1987 Buick Park Ave | 23 | ± | 4 | 40 | ± | 4 | 63 | ± | 7 |
| Car | 81-90 | Catalyst | 1987 Acura Integra | 51 | ± | 6 | 21 | ± | 2 | 73 | ± | 7 |
| Car | 81-90 | Catalyst | 1986 Chrysler 5th Ave | 47 | ± | 6 | 79 | ± | 8 | 126 | ± | 14 |
| Car | 81-90 | Catalyst | 1986 Alfa Romeo Spider | 63 | ± | 9 | 21 | ± | 3 | 84 | ± | 12 |
| Truck | 81-90 | Catalyst | 1985 Toyota Pick-up | 51 | ± | 8 | 17 | ± | 3 | 68 | ± | 11 |
| Car | 81-90 | Catalyst | 1985 Oldsmobile Cutlass | 46 | ± | 5 | 15 | ± | 2 | 61 | ± | 6 |
| Truck | 81-90 | Catalyst | 1985 Dodge Caravan | 57 | ± | 8 | 6 | ± | 1 | 63 | ± | 8 |
| Car | 81-90 | Catalyst | 1985 Chevy Caprice | 71 | ± | 8 | 10 | ± | 2 | 82 | ± | 9 |
| Car | 81-90 | Catalyst | 1985 Chevrolet Sprint | 69 | ± | 9 | 13 | ± | 2 | 82 | ± | 11 |
| Car | 81-90 | Catalyst | 1984 Nissan Sentra | 33 | ± | 3 | 36 | ± | 5 | 69 | ± | 7 |
| Car | 81-90 | Catalyst | 1984 Mazda 626 | 74 | ± | 7 | 28 | ± | 3 | 102 | ± | 10 |
| Truck | 81-90 | Catalyst | 1984 Dodge Ram | 70 | ± | 8 | 12 | ± | 1 | 82 | ± | 8 |
| Car | 81-90 | Catalyst | 1984 Buick Regal LTD | 31 | ± | 4 | 12 | ± | 2 | 43 | ± | 6 |
| Truck | 81-90 | Catalyst | 1981 Chevrolet G-10 | 78 | ± | 11 | 10 | ± | 2 | 88 | ± | 12 |
| Truck | 81-90 | Catalyst | 1981 Chevrolet C-10 | 24 | ± | 4 | 93 | ± | 14 | 117 | ± | 16 |
| Car | 65-80 | Catalyst | 1980 Honda Prelude | 54 | ± | 5 | 14 | ± | 1 | 68 | ± | 7 |
| Truck | 65-80 | Catalyst | 1980 Ford E350 Van | 89 | ± | 10 | 8 | ± | 1 | 97 | ± | 10 |
| Car | 65-80 | Catalyst | 1979 Plymouth Horizon | 68 | ± | 7 | 4 | ± | 0 | 72 | ± | 7 |
| Car | 65-80 | Catalyst | 1979 Nissa 280ZX | 42 | ± | 5 | 43 | ± | 4 | 85 | ± | 9 |
| Car | 65-80 | Catalyst | 1979 Ford Mustang | 69 | ± | 9 | 23 | ± | 3 | 92 | ± | 13 |
| Car | 65-80 | Catalyst | 1978 Toyota Corolla | 69 | ± | 8 | 37 | ± | 6 | 106 | ± | 11 |
| Car | 65-80 | Catalyst | 1978 Pontiac LeMans | 95 | ± | 9 | 8 | ± | 1 | 102 | ± | 11 |
| Truck | 65-80 | Catalyst | 1978 Chevrolet C-20 PU | 76 | ± | 10 | 4 | ± | 1 | 80 | ± | 11 |
| Car | 65-80 | Catalyst | 1977 Datsun 200 SX | 37 | ± | 4 | 34 | ± | 3 | 70 | ± | 7 |
| Car | 91-00 | Diesel | 1993 Mercedes 300D | 13 | ± | 2 | 70 | ± | 7 | 83 | ± | 9 |
| Car | 81-90 | Diesel | 1985 Mercedes 300D | 88 | ± | 10 | 89 | ± | 9 | 177 | ± | 18 |
| Car | 81-90 | Diesel | 1984 Volkswagen Rabbit | 14 | ± | 2 | 61 | ± | 6 | 75 | ± | 8 |
| Car | 81-90 | Diesel | 1984 Toyota Corolla | 9 | ± | 1 | 76 | ± | 7 | 85 | ± | 9 |
| Car | 81-90 | Diesel | 1984 Mercedes 300D | 9 | ± | 1 | 89 | ± | 9 | 98 | ± | 10 |
| Truck | 81-90 | Diesel | 1982 Volkswagen Vanagon | 21 | ± | 2 | 56 | ± | 6 | 78 | ± | 8 |
| Car | 81-90 | Diesel | 1982 Volkswagen Rabbit | 32 | ± | 4 | 37 | ± | 4 | 69 | ± | 7 |
| Car | 81-90 | Diesel | 1982 Mercedes Benz | 28 | ± | 3 | 38 | ± | 4 | 66 | ± | 7 |
| Car | 81-90 | Diesel | 1982 Mercedes 300 TD | 11 | ± | 1 | 102 | ± | 10 | 113 | ± | 11 |
| Car | 81-90 | Diesel | 1982 Isuzu I-Mark | 17 | ± | 2 | 59 | ± | 6 | 76 | ± | 8 |
| Car | 81-90 | Diesel | 1981 Peugeot 505 TD | 11 | ± | 1 | 48 | ± | 5 | 59 | ± | 6 |
| Car | 81-90 | Diesel | 1981 Mercedes 300 SD | 12 | ± | 1 | 72 | ± | 7 | 84 | ± | 9 |
| Car | 65-80 | Diesel | 1980 Volkswagen Rabbit | 22 | ± | 2 | 57 | ± | 6 | 78 | ± | 8 |
| Car | 65-80 | Diesel | 1980 Mercedes 300 TD | 42 | ± | 5 | 17 | ± | 2 | 59 | ± | 6 |
| Car | 65-80 | Diesel | 1980 Mercedes 240D | 22 | ± | 3 | 45 | ± | 4 | 67 | ± | 7 |
| Car | 65-80 | Diesel | 1979 Volswagen Rabbit | 51 | ± | 6 | 13 | ± | 1 | 64 | ± | 6 |
| Car | 65-80 | Diesel | 1977 Mercedes 300D | 18 | ± | 2 | 40 | ± | 4 | 57 | ± | 6 |
| Car | 65-80 | No Catalyst | 1979 Honda Civic | 39 | ± | 6 | 20 | ± | 3 | 59 | ± | 9 |
| Truck | 65-80 | No Catalyst | 1973 Ford Ranger | 83 | ± | 11 | 3 | ± | 0 | 86 | ± | 12 |
| Truck | 65-80 | No Catalyst | 1972 Chevy C-20 Pick-Up | 69 | ± | 8 | 5 | ± | 0 | 74 | ± | 8 |
| Car | 65-80 | No Catalyst | 1965 Ford Mustang | 73 | ± | 10 | 4 | ± | 1 | 77 | ± | 11 |

Table 7.  Emissions in Tons per Day
Based on Vehicle Miles Traveled in Thousands

| Year Group | Light Duty Passenger Cars | Light Duty Trucks |
| --- | --- | --- |
|  | Non-cat | Cat | Diesel | Total | Non-cat | Cat | Diesel | Total |
| 91-00 | 0 | 26216 | 26 | 26242 | 0 | 18727 | 512 | 19239 |
| 81-90 | 0 | 10856 | 118 | 10975 | 0 | 6790 | 283 | 7073 |
| 65-80 | 829 | 771 | 51 | 1652 | 1202 | 918 | 19 | 2139 |
| 65-00 | 829 | 37844 | 195 | 38869 | 1202 | 26435 | 814 | 28451 |

Table 8.  Elemental and Organic Carbon for Cars and Trucks
Grouped by Year (Weight Percent Mass)

| Vehicle Type | Year Bin | OC | EC | TC |
| --- | --- | --- | --- | --- |
| Cars | 91-00 | 36 | ± | 17 | 44 | ± | 20 | 81 | ± | 36 |
| Cars | 81-90 | 42 | ± | 22 | 31 | ± | 25 | 72 | ± | 25 |
| Cars | 65-80 | 58 | ± | 22 | 18 | ± | 13 | 76 | ± | 14 |
| Cars | 65-00 | 38 | ± | 19 | 39 | ± | 21 | 78 | ± | 32 |
| Trucks | 91-00 | 30 | ± | 28 | 57 | ± | 35 | 86 | ± | 29 |
| Trucks | 81-90 | 64 | ± | 26 | 21 | ± | 27 | 85 | ± | 24 |
| Trucks | 65-80 | 78 | ± | 10 | 5 | ± | 2 | 83 | ± | 11 |
| Trucks | 65-00 | 42 | ± | 26 | 44 | ± | 30 | 86 | ± | 27 |
| Cars and Trucks | 65-00 | 40 | ± | 22 | 41 | ± | 25 | 81 | ± | 30 |

## Wood Combustion

Residential and agricultural burning emissions were sampled as part of the “Development of a Gas and Particulate Matter Organic Speciation Profile Database”.  The residential wood combusion samples included oak, tamarack, eucalyptus, and almond.  The agricultural burning included rice and wheat.

Since the oak and eucalyptus samples showed similar chemical composition, they were averaged together to represent variability from different source subtypes.  The almond sample was similar to the oak and eucalyptus for most of the species, but showed major difference in the abundances of the carbon fractions.  The tamarack differs from other wood burning profiles by having more elemental carbon and less organic carbon.  Figures 1 and 2 show chemical composition of wood burning samples.

Since rice and wheat samples showed significant differences in chemical composition, they were retained as individual profiles.

Figure 1.  Source Profiles for Oak and Eucalyptus
(Selected Species Only)

Figure 2.  Source Profiles for Almond and Tamarack
(Selected Species Only)

Figure 2.  Source Profiles for Wheat and Rice
(Selected Species Only)