## Slide 1: Aiming at the increase of California’s ethanol ‘blend wall’: gaseous and particulate emissions evaluation from a fleet of GDI and PFI vehicles operated on E10 and E15 fuels
Tianbo Tang, Thomas D. Durbin, Kent C. Johnson, Georgios Karavalakis
Center for Environmental Research and Technology
University of California, Riverside

## Slide 2
After graduating with an M.S. in Environmental Engineering at USC, I joined the Emissions and Fuels Research group at CE-CERT, UCR in 2019 as a Ph.D student
Over the past three years I have worked on various projects to understand emissions from various alternative and renewable fuels to help legislative parties to determine future regulations
Presenter Background

## Slide 3: Motivation
Ethanol has been promoted in the US as the biofuel of choice through several mandates (i.e., RFS, EISA)
The US EPA allows E15 fuel to be sold year-round across the US
CARB considers to increase the ethanol blend limit from E10 to E15 in California
  Ethanol is produced from renewable sources, which will result in more low-carbon fuel in the transportation sector and less petroleum gasoline consumption
  Reduction of harmful pollutants and GHGs
      There is limited data on the emission impacts of E15 from current PFI and GDI vehicles

## Slide 4: Test Setup
FTP test cycle

## Slide 5: Vehicle Specifications
Vehicle descriptions (20) | 11 GDI vehicles, 6 PFI vehicles, 2 PFI+GDI vehicles and 1 PFI plug-in Hybrid vehicle
Year | 2016-2021
Vehicle class (EPA) | LDV and LDT
Engine size (L) | 1.4 L to 5.7 L
AIR system | 3 Turbocharged vehicles + 17 Naturally aspirated vehicles
Number of cylinders | 4 to 8
Engine compression ratio | 9.3:1 to 13:1
Technology group (CA) | 5 SULEV30 + 5 ULEV50 + 5 ULEV70 + 5 ULEV125
Aftertreatment systems | All vehicles equipped with TWC + 3 vehicles equipped with EGR

## Slide 6: Test Fuels
Property | Test Method | Unit | E10-avg | E15-avg
RVP (EPA Equation) | D5191 | psi | 7.43 | 7.35
Research Octane Number | D2699Mdp | ON | 91.13 | 93.63
Motor Octane Number | D2700Mdp | ON | 83.53 | 85.07
API Gravity | D4052 |  | 59.15 | 58.48
Heat of Combustion, Gross | D4809 | BTU/lb. | 19264 | 18877
 |  | MJ/kg | 44.81 | 43.91
 |  | cal/g | 10702 | 10487
Heat of Combustion, Net |  | BTU/lb. | 17982 | 17605
 |  | MJ/kg | 41.83 | 40.95
 |  | cal/g | 9990 | 9780
Ethanol |  | Vol% | 9.66 | 14.45
Total Oxygen |  | wt.% | 3.59 | 5.35
Carbon | D5291 CH | wt.% | 82.80 | 80.91
Hydrogen |  | wt.% | 14.05 | 13.94
Sulfur | D5453 | ppm | 6.25 | 4.47
Benzene | D5580 | Vol% | 0.60 | 0.56
Toluene |  | Vol% | 4.04 | 3.81
Ethylbenzene |  | Vol% | 0.94 | 0.89
p,m-Xylene |  | Vol% | 3.85 | 3.65
o-Xylene |  | Vol% | 1.36 | 1.29
C9 plus Aromatics |  | Vol% | 8.74 | 8.26
Total Aromatics |  | Vol% | 19.53 | 18.46
Olefin | D6550 | Mass % | 5.03 | 4.63
Distillation | D86 |  |  | 
IBP |  | deg F | 101.63 | 102.27
10% |  | degF | 135.33 | 136.00
50% |  | degF | 204.50 | 161.13
70% |  | degF | 248.70 | 244.00
90% |  | degF | 313.63 | 310.50
Final Boiling Point |  | degF | 394.07 | 393.93
Particulate Matter Index (Aikawa et al.) |  |  | 1.15 | 1.10

## Slide 7: Driving Cycle, Test Protocol and Statistical Analysis
Emissions and fuel economy measurements were conducted over triplicate FTP cycles.
The fuel testing sequence was randomized for every vehicle.
The test vehicles were preconditioned with a procedure including:
  Fuel drain and fill (40%)
  HWFET
  Fuel drain and fill (40%)
  HWFET
  2 LA4s
Statistical analyses for each pollutant were run using the mixed procedure in PC/SAS from SAS Institute, Inc. The fuel type was treated in the model as a fixed factor and the vehicles as a random factor
  The results from the natural logarithms (ln) or inverse models were “back transformed” to provide least square means (LSMs) for all pollutants on each fuel
  This provides an arithmetic value to evaluate the magnitude of statistically significant effects
  We define when p≤0.05, it is at statistically significant level. When 0.05<p≤0.1, it is at marginally statistically significant level

## Slide 8: Gaseous emissions
For NOx emissions, a decreasing trend for more stringent regulations was observed
For THC weighted emissions, E15 was 5% lower than E10 at statistically significant level
For CO weighted emissions, E15 was 17% lower than E10 at statistically significant level
For NMHC weighted emissions, E15 was 8% lower than E10 at marginally statistically significant level
NOx and CO2 did not show statistically significant difference between E10 and E15
LSM

## Slide 9: MSAT
For ethylbenzene emissions, E15 showed 11% decrease compared to E10 at statistically significant level
For m/p-xylenes emissions, E15 showed 10% reduction compared to E10 at marginally statistically significant level
For o-xylene emissions, E15 showed 9% reduction compared to E10 at marginally statistically significant level
For ethanol emissions, E15 showed 77% increase compared to E10 at statistically significant level
For acetaldehyde emissions, E15 showed 32% increase compared to E10 at statistically significant level
LSM

## Slide 10: NMOG
Similar trend compared to NOx emissions. A decreasing trend for more stringent regulations

## Slide 11: Ozone Forming Potential
E15 trends lower for OFP
Newer vehicles led to lower OFP, with the more efficient GDIs showing lower OFP than PFIs

## Slide 12: PM mass emissions
Lower emissions for PFI vehicles compared to GDI vehicles
Lower trend for E15 compared to E10
For weighted emissions, E15 showed 18% reduction compared to E10 at statistically significant level
For cold start (ph1) emissions, E15 showed 17% reduction compared to E10 at statistically significant level
For hot running (ph2) emissions, E15 showed 54% reduction compared to E10 at statistically significant level
For hot start (ph3) emissions, E15 showed 43% reduction compared to E10 at marginally statistically significant level
LSM

## Slide 13: Solid Particle Number Emissions
Weighted SPN (>23nm) emissions showed a statistically significant reduction of 12% for E15 compared to E10.
Overall, high concentrations of sub-23nm SPN emissions were observed for all vehicles
LSM

## Slide 14: Particle Size Distributions
For weighted PSD, significantly higher particle populations in the accumulation (soot) mode for the GDI vehicles compared to PFI vehicles
  Accumulation mode particles were centered at about 52-60nm and 52nm for the GDI and PFI vehicles, respectively
  E15 resulted to lower particle diameters
E15 showed decreasing trend for different phases of FTP for both GDI and PFI vehicles
Cold-start
Hot-running
Hot-start
Weighted

## Slide 15: Summary
Overall, E15 showed statistically significant reductions on THC, CO, and NMHC emissions compared to E10
PM mass emissions showed strong statistically significant reductions for E15 across the 20 vehicle fleet
No strong statistically significant fuel effects were observed for NOx
The introduction of E15 will likely reduce air toxics from current technology vehicles and will not lead to air quality degradation in California
Particle number emissions showed statistically significant reductions for E15 compared to E10
Ozone forming potential trended lower for E15 compared to E10

## Slide 16: Acknowledgments
We acknowledge funding from the California Air Resources Board, Renewable Fuels Association, Growth Energy, National Corn Growers Association, and the United States Council for Automotive Research (USCAR)

## Slide 17: Thank you!

## Slide 18: Test Vehicles
 | PFI#1 | GDI#1 | PFI#2 | PFI#3 | PFI+GDI#1 | GDI#2 | GDI#3 | GDI#4 | GDI#5 | PFI#4 | GDI#6 | PFI#5 | GDI#7 | PFI_Hybrid#1 | GDI#8 | GDI#9 | GDI#10 | PFI+GDI#2 | PFI#6 | GDI#11
Year | 2019 | 2018 | 2020 | 2016 | 2019 | 2018 | 2016 | 2020 | 2019 | 2021 | 2020 | 2020 | 2020 | 2020 | 2020 | 2020 | 2021 | 2017 | 2021 | 2018
Make | Dodge | Honda | Jeep | Nissan | Toyota | Honda | Mazda | Ford | Chevrolet | Chevrolet | KIA | Jeep | Nissan | Toyota | GMC | Buick | Chevrolet | Ford | Hyundai | Chevrolet
Model | Ram1500 | Fit | Compass | Rogue | Rav4 | Civic | Mazda3 | Fusion | Impala | Spark | Optima | Cherokee | Armada | Prius | Acadia | Enclave | Colorado | F-150 | Accent | Suburban
Miles at start (mi) | 32234 | 35547 | 29174 | 63491 | 37329 | 35776 | 74339 | 33029 | 25728 | 4073 | 29377 | 23272 | 32731 | 10015 | 34942 | 32621 | 17603 | 7352 | 12226 | 34477
Engine size (L) | 5.7 | 1.5 | 2.4 | 2.5 | 2.5 | 1.5 | 2.5 | 2 | 3.6 | 1.4 | 2.4 | 3.6 | 5.6 | 1.8 | 3.6 | 3.6 | 3.6 | 3.5 | 1.6 | 5.3
Fuel injection type | PFI | GDI | PFI | PFI | GDI+PFI | GDI | GDI | GDI | GDI | PFI | GDI | PFI | GDI | PFI | GDI | GDI | GDI | GDI+PFI | PFI | GDI
AIR system | NA | NA | NA | NA | NA | Turbo | NA | Turbo | NA | NA | NA | NA | NA | NA | NA | NA | NA | Turbo | NA | NA
Emission standard | USEPA: T3 B70 CA: ULEV70 | USEPA: T3B30 CA: SULEV30 PC | USEPA: T3 B50 CA: ULEV50 | USEPA: For sale only in states with California emission standards CA: LEV3-ULEV70 | USEPA: T3B50 CA: ULEV50 | USEPA: IT3B125 CA: ULEV125 PC | USEPA: N/A CA: SULEV30/PZEV | USEPA: T3B70 CA: ULEV70 PC | USEPA: TIER3 CA: PC/SULEV30 | USEPA: TIER3 CA: PC/ULEV70 | USEPA: T3B70 CA: ULEV70 PC | USEPA: T3 B30 CA: SULEV30 | USEPA: T3 B125 CA: LEV3-ULEV125 | USEPA: T3 B30 CA: SULEV30 PC | USEPA: TIER3 CA: ULEV50 | USEPA: TIER3 CA: ULEV50 | USEPA: TIER3 CA: ULEV50 | USEPA: T2B5 CA: ULEV125 | USEPA: T3B125 CA: ULEV125 PC | USEPA: TIER3 CA: ULEV125